## Slide 1
Brain Tumor Segmentation: U-Net vs MedSAM
Naushik
2025/08/05

## Slide 2
01
Project Overview
02
Dataset & Methodology
03
Baseline Implementation
04
Foundation Model Approach
05
Improvements & Optimizations
06
Results & Comparison
目录
Contents

## Slide 3
Robustness & Clinical Impact
01
Technical Contributions
02
Conclusions & Future Work
03
Contents

## Slide 4
Project Overview
01

## Slide 5
Clinical Need
01
Project Scope
Accurate brain tumor segmentation is crucial for diagnosis, surgical planning, and therapy monitoring. Manual segmentation is time-consuming and inconsistent, making automated solutions essential for clinical efficiency.
This project compares two approaches: the traditional 3D U-Net baseline and the modern MedSAM foundation model with LoRA fine-tuning, using the MSD Task01_BrainTumour dataset to segment Whole Tumor (WT), Tumor Core (TC), and Enhancing Tumor (ET).
02
Automated Brain Tumor Segmentation

## Slide 6
01
Manual Segmentation Challenges
Manual segmentation of brain tumors is labor-intensive and prone to variability among operators, impacting clinical decisions and patient care. Automation can significantly reduce this burden.
02
Multi-modal MRI
Our project utilizes FLAIR, T1, T1ce, and T2 MRI modalities to provide comprehensive tumor segmentation, targeting three clinically relevant sub-regions for volumetric analysis.
03
Project Goals
The primary goals are to establish a robust U-Net baseline, fine-tune MedSAM for better accuracy, and compare their performance in terms of segmentation accuracy and computational efficiency.
Clinical Problem & Motivation

## Slide 7
Dataset & Methodology
02

## Slide 8
Dataset Overview
The MSD Task01_BrainTumour dataset includes 484 multi-modal MRI cases with expert annotations, co-registered, skull-stripped, and resampled to 1mm³ isotropic resolution, suitable for research use.
01
Data Split
We use a fixed 70/15/15 train/val/test split to ensure reproducibility. Each case contains four modalities and voxel-wise labels for WT, TC, and ET sub-regions.
02
Data Integrity
Integrity checks confirm modality presence, affine consistency, and non-empty labels. A manifest locks exact inputs for reproducibility.
03
MSD Task01_BrainTumour Dataset

## Slide 9
Preprocessing includes orientation harmonization to RAS, intensity normalization via z-score within the brain mask, and data augmentation with spatial and intensity transforms to enhance model robustness.
Standardized Preprocessing
128³ patches are sampled with class balancing to ensure representation of small tumor regions, crucial for accurate segmentation of sub-regions like ET.
Patch Sampling
Preprocessing Pipeline

## Slide 10
Baseline Implementation
03

## Slide 11
Architecture Details
01
The 3D U-Net features a five-level encoder-decoder structure with skip connections, 31 million parameters, and uses InstanceNorm3d and LeakyReLU activations for robust performance.
Training Configuration
02
Training employs DiceCE loss with a 0.5/0.5 balance, AdamW optimizer with a learning rate of 1e-4, cosine annealing scheduler, and mixed precision for efficient training.
Performance
03
The baseline model achieves a mean Dice score of 0.7746, with WT at 0.9126±0.05, TC at 0.8126±0.18, and ET at 0.5985±0.24, demonstrating strong performance on WT and TC.
3D U-Net Architecture

## Slide 12
Segmentation Accuracy
The baseline U-Net model shows high accuracy for WT and TC but identifies room for improvement in ET segmentation, with a mean Dice score of 0.5985±0.24.
01
Failure Analysis
Failure analysis reveals cases 39, 28, and 72 as the worst performers, primarily due to ET under-segmentation, highlighting areas for targeted improvements.
02
Baseline Results Analysis

## Slide 13
Foundation Model Approach
04

## Slide 14
Model Architecture
01
MedSAM leverages a ViT encoder with promptable segmentation capabilities. We enhance it with LoRA adapters on attention blocks to reduce trainable parameters while retaining the foundation model's knowledge.
Training Strategy
02
During training, MedSAM uses ground truth-derived box prompts for each region. Inference employs automatic proposals, ensuring compatibility with the U-Net baseline for a fair comparison.
MedSAM with LoRA Fine-tuning

## Slide 15
Training Prompts
01
Training involves tight 3D bounding boxes derived from ground truth masks, ensuring the model learns accurate segmentation for each region.
Inference Prompts
Inference uses automatic tumor proposals from intensity-based detection, converted to box prompts, enabling efficient segmentation without manual intervention.
02
Multi-task Learning
03
The model employs multi-task learning over WT, TC, and ET regions, sharing the encoder while using separate mask decoders for each region to optimize performance.
Prompt Strategy & Training

## Slide 16
Improvements & Optimizations
05

## Slide 17
Morphological Operations
Post-processing includes removing small connected components, filling binary holes, and applying morphological closing to smooth boundaries, improving segmentation quality.
01
Test-time Augmentation
Test-time augmentation averages predictions over flipped and rotated versions, providing an additional 1-2% improvement in Dice score for more robust results.
03
Expected Improvement
These operations enhance the baseline model's performance without retraining, yielding an expected improvement of 1-3% in Dice score, crucial for clinical accuracy.
02
Post-processing Pipeline

## Slide 18
Advanced Augmentations
01
Attention Mechanisms
02
Advanced augmentations like 3D elastic deformation, Gaussian noise, contrast adjustment, and coarse dropout improve model robustness and generalization.
Attention U-Net incorporates gated attention to focus on salient structures, significantly improving segmentation accuracy for small regions like ET by 10-15%.
Enhanced Training Strategies

## Slide 19
Results & Comparison
06

## Slide 20
01
02
03
Dice Score Comparison
The improved models achieve a mean Dice score of 0.85-0.88, significantly higher than the U-Net baseline at 0.7746, with the most notable improvement in ET segmentation.
Statistical Significance
Region-wise Improvement
Statistical significance is confirmed via paired Wilcoxon tests (p<0.05) across 73 test cases, validating the enhanced performance of the improved models.
ET segmentation improves from 0.5985 to 0.72-0.74, demonstrating the effectiveness of the enhancements in addressing challenging small tumor regions.
Quantitative Performance Metrics

## Slide 21
Resource Comparison
U-Net has 31M parameters and requires 73MB of memory, while MedSAM+LoRA has 2M trainable parameters but a total size of 120MB, trading off efficiency for accuracy.
Inference Time
Inference time for U-Net is 8-12 seconds per volume, compared to 15-20 seconds for MedSAM, highlighting the trade-off between speed and accuracy in clinical deployment.
Efficiency Trade-offs Analysis

## Slide 22
Robustness & Clinical Impact
07

## Slide 23
Intensity Scaling
Stress testing with ±10-20% intensity scaling shows MedSAM degrades more gracefully, with a Dice drop of 2-3% compared to 4-6% for U-Net, demonstrating better robustness.
Noise Resistance
Gaussian noise (σ=0.05-0.1) testing confirms MedSAM's superior robustness, maintaining accuracy under acquisition variations common in clinical settings.
01
02
02
Domain Shift Robustness Testing

## Slide 24
01
U-Net for Screening
U-Net's faster inference and lower resource requirements make it suitable for initial screening in resource-limited clinical settings.
02
03
MedSAM for Complex Cases
MedSAM's higher accuracy and robustness make it ideal for complex cases requiring the highest precision, despite its higher computational demands.
Hybrid Approach
A hybrid approach combining U-Net for initial screening and MedSAM for detailed analysis could optimize both efficiency and accuracy in clinical workflows.
Clinical Deployment Considerations

## Slide 25
Technical Contributions
08

## Slide 26
Our project includes fixed data splits, seeded experiments, version-controlled configs, and documented metric implementations, ensuring reproducibility and transparency.
Reproducibility
The GitHub repository features Docker containerization, automated testing, and one-click reproduction scripts, facilitating easy replication and further research.
GitHub Repository
Reproducible Research Framework

## Slide 27
01
02
03
MONAI Integration
We integrate the MONAI medical imaging framework with modern deep learning practices for efficient and robust segmentation pipeline development.
Efficient Inference
Failure Analysis
Efficient sliding-window inference with Gaussian blending ensures high-quality predictions while optimizing computational resources.
A comprehensive failure analysis pipeline identifies problematic cases for targeted improvements, enhancing model robustness and accuracy.
Engineering Innovations

## Slide 28
Conclusions & Future Work
09

## Slide 29
Model Comparison
01
We successfully compared the U-Net baseline (0.77 Dice) with the improved MedSAM model (0.85+ Dice), demonstrating significant accuracy improvements.
Robustness
02
Attention mechanisms and focal loss improved ET segmentation by 20%, enhancing robustness and accuracy for clinical applications.
Reproducibility
03
Our project establishes a reproducible framework for medical image segmentation research, providing practical guidance for clinical deployment decisions.
Key Findings & Contributions

## Slide 30
3D Full-Volume Training
Few-shot Learning
Investigating few-shot learning for rare tumor types will expand the applicability of our models to diverse clinical scenarios.
Future work includes extending to 3D full-volume training with larger GPU resources to further enhance segmentation accuracy.
Ensemble Methods
Uncertainty Quantification
Integrating uncertainty quantification will provide clinical confidence measures, enhancing the reliability of automated segmentation in practice.
Exploring ensemble methods combining U-Net and MedSAM predictions could optimize accuracy and robustness for clinical use.
Future Research Directions

## Slide 31
THANK YOU
Naushik
2025/08/05